## Slide 1: Chemically Challenged Sediment Dredging in Los Angeles Jim Fields Los Angeles District USACE

## Slide 2: What We Have Done/Tried
CAD Site Geo-tubes and Capping
Pilot Studies
  Cement Stabilization
  CAD Site
  Sediment Washing
  Sediment Blending
Sediment Separation
Upland
CDF’s

## Slide 3: CAD Site Geo-tubes and Capping
One of our (LA District) first attempts at dealing with Contaminated sediments.
Lined dump scows with Geo-Fabric placed Contaminated sediment in the scow and sewed it up
Dumped the tube and buried it with clean cover material

## Slide 4: Pilot Studies
WHAT ARE WE GOING TO DO???
Possible Alternatives for Future
Continue Marching Forward While Investigating
  Cement Stabilization
  CAD Site
  Sediment Washing
  Sediment Blending

## Slide 5: Cement Stabilization
Add Cement or Fly Ash
Small Percent Great Geotechnical Result
Dry additive didn’t work, add in slurry form
Labor intensive
Fast acting
pH Change mobilized some metals
Bench testing required

## Slide 9: CDF’s
Easiest answer for now contaminants Removed from the Environment
Timing issues who has Envir. Clearances and Funding to match up with others schedules
Finite amount of space available
On-Site Coordination/Management objectives need to be met

## Slide 11: CAD Site
Great deal of opposition
  If you remove once take it out
    Lose quantity cost 25% removed at same price
Environmentally accepted other regions
Locations available
Small Pilot Test
  Showed good results in subsequent monitoring
We still need a caretaker

## Slide 13: Sediment Washing Sediment Blending
These were both Bench scale and Litriture investigations
SW- Requires a large area and a lot of clean water to flush out contaminates as well as time for contaminants to dissociate/release
SB- Take Good Sediment and bad sediment and try to make a mediocre sediment out of it by mixing typically with bulldozers and discs

## Slide 14: Sediment Separation
Initial stages of development
Contaminants bind to the Fines
Issues handling Trash & Organics
Volume leveling issues can’t keep up with big dredges
Getting other agency buy in
How clean is clean and by what basis
ER-L, ER-M, Trophic trace model